MC3-E Flight Engineer Checklist - Updated April 16, 2011

# Before Flight

## Set watch to current GMT time.

## Have digital camera.

## Have USB sticks and PCMCIA cards.

## Have note books with check list.

Remove CPC Butanol Bottle.

Set Nevzorov control box to the correct settings for the chosen hotwire temperatures.

# Before Engine Start:

## Make sure memory card is in the Applanix Unit.

## Make sure PCMCIA card is in the M300.

# After Engine Start:

## Push all AC breakers

## M300 Power – On

Push in DC instrument and anti-ice breakers

Applanix Power – On

## TDL and Back-Right Rack Power Bar – On

## Run timesync.awk script on M300 computer – ‘./home/bypass/timesync.awk’

Start M300 software – type ‘go’ into a terminal window

Data File Check (Check that data is being saved to hard disk).

Bring up M300 Status Window (Use F1 to select), note data <filename>.

Bring up terminal window, ‘cd /2010/m300data’, ls –l <filename>, note size.

Ensure a file being written to (F1 screen) and that its size is not zero.

## Tell Pilots: Ready to Taxi

## M300 F3 Status Checks

Check static pressure, note value.

### Check air temperature, note value.

### Check dew point temperature, note value.

### Check Goodrich OIDC Power Switch, note position.

Check Goodrich OIDC gain switch settings (three switches), note positions.

Check Goodrich Optical Ice Detector, note voltage values (< 0.7 volts)

### Check CDP, note reference voltage (~ 5.0 volts).

### Check CPC, note average concentration, ‘No CPC Data Interval’ (1), and flow rate (~1 Lpm).

### Check Laser Hygrometer, note dew point temp and flow rate (~ 8.5 Lpm).

### Check the 2-DC; note the End Element voltages (> 0.5 volts)

Check Serial Data Screen, note data acquisition status

Check Goodrich Ice Detector, note MSO Frequency and Operational State

Check CIP, note Diode Voltages

# Before Takeoff:

## Open the shutter for the Goodrich Optical Ice Detector.

Check that Overflow light on Goodrich OID goes out (If not, cycle power)

# After Takeoff:

## King Probe power switch and Heater switch– On

## Nevzorov Power and Heaters – On

Note temperature settings on Nevzorov box

Note voltage values for all 8 connectors (>0.0 volts)

## Before Landing:

## King Probe – Off

## Nevzorov – Power and Heaters Off

# After Landing:

## Close the shutter for the Goodrich Optical Ice Detector.

## M300 Data System

### Quit M300 Software File/Exit (Do not save when asked).

Turn M300 off

## Applanix – Off

## DC power breakers – Out

## Check all computers are off

## Pull all AC breakers

## Ensure the shutter for the Goodrich Optical Ice Detector is closed.  Note position.

# After Flight

## Copy M300 flight data onto PCMCIA card (/dos/c directory).

## Remove M300 and Applanix PCMCIA card from airplane.

| Command | Description | Command | Description |
| --- | --- | --- | --- |
| Alt F1 | Hide Window | CTL F1 | PCASP Pump |
| F1 | Control Window | CTL F2 | Pitot Selection |
| F2 | Profiles | CTL F7 | Map Zoom In |
| F3 | Text Display | CTL F8 | Map Zoom Out |
| F4 | Strip Charts 1 | CTL F9 | Map Center |
| F5 | Strip Charts 2 | CTL F10 | Clear Map |
| F6 | Spectrum Plots | CTL F11 | Previous Desktop |
| F7 | Flight Track | CTL F12 | Next Desktop |
| F8 | Combine Spectrum | CTL ALT F1 | Shutdown |
| F9 | 2D Images | CTL ALT F5 | Quit |
| F10 | Help Screen |  |  |
| F11 | Main Screen |  |  |
| F12 | M300 Logger |  |  |

| KVM Switch # | Computer |
| --- | --- |
| 1 | CPI |
| 2 | HVPS-3 |
| 3 | UHSAS |

Manually Update M300 time:  quit M300 software and adjust time (su && date HHMM.SS && rtc –s hw && exit), restart m300 software

# MC3-E CPI, UHSAS, & HPVS-3 Flight Engineer Checklist - Updated April 16, 2011

# After Engine Start:

## CPI Computer, HVPS-3, and UHSAS computers – On

Wait for M300 computer to fully boot

Set up UHSAS Probe

Run Sync_Time_UND.bat script (syncs time with the M300)

Double-click on UHSAS.vi icon on Desktop

Make sure computer is communicating with probe (Probe Temp is increasing)

HVPS-3

Run Sync_Time_UND.bat script (syncs time with the M300)

Double click HVPS software icon on desktop (Spec2d.exe?)

Turn HVPS power switch on face of computer to ON

In HVPS software, Click on red triangle ‘Record’ button, note file name.

Check getting TAS from M300 computer

## CPI System

Run Sync_Time_UND.bat script

CPI Power Supply – On

Communications test

#### Open PC2MA test software (icon on desktop)

#### Go to File, then click GO

#### If test does not respond, restart computer only and run PC2MA again

#### After PC2MA responds, close PC2MA

Start CPI software

Set laser settings under Settings:

#### PDS45 laser, PDS90 laser, & Main laser:  4095   Spectral Width: 2048.

Click on Start Probe button

## UHSAS

Verify Scatter Voltage is varying

Note sample and sheath flow rates

Note Reference and Scatter voltages and Probe Temperature.

Switch to Histogram tab, click Run, click Record (make sure Record is dark grey)

Note integration time (change to 1 sec if greater than 1 sec).

# After Takeoff:

## Verify HVPS-3 TAS matches M300 TAS.

# After Landing:

## UHSAS –

Click off Record (should be light grey now)

Click “STOP”

Shut down computer

## HVPS-3 –

Hit “Stop” button (Red circle w/ ‘X’ in middle)

Click “File”, then “Exit”

Shut down probe and computer

## CPI – Stop data acquisition, exit data acquisition software, shut down probe and computer

## PMS Probes – Off (Pull Breakers)

# After Flight:

## Copy UHSAS, HVPS-3, and CPI data onto their respective flash drives.

## Transfer data from flash drives to laptops