MPACE Field Project Checklist - Updated September 20, 2004

Before Flight

Set watch to current GMT time

Have 8mm tape, floppy disk and video tape

Before Engine Start:

Make sure TAMDAR DC power breaker is pulled out.

Make sure memory card is in the Applanix Unit

Wet and install pads in CCN counter

After Engine Start:

Research Power - On

Applanix Power - On

M200 Data System Power – On

TAMDAR DC power breaker – In

TDL Power – On

TDL Pump Power – On

CCN Counter Power – ON

M200 Data System

Exabyte Tape – In

Set Time

Type: cd 2004\mpace

Type: m200

Applanix System

Start Data Logging  (Press “Log Data” button twice, wait one second 	 in between each press)

Video Systems

VCR Power on

Load VHS tape in VCR

Set Time

Press Play/Record

Status Check

Check M200 System Time to make sure it agrees with GPS Time

(If not, quit M200 software and adjust time, restart m200 software)

Before Takeoff:

PMS Probes – On (L/OTR, L/INB, R/OTR, R/INB – 2 clicks)

After Takeoff:

King Probe and Heater – On

Before Landing:

King Probe – Off

PMS Probes – Off

After Landing:

VCR – Stop, Eject Tape

TAMDAR – Close “Data Acquisition” Program

Shutdown Computer – Start, Shut Down

Applanix System – Stop Logging Data (Press “Log Data” twice, wait one second between each press)

M200 Data System – Type: quit

Type: pkzip a:ddmmyya.zip mike.asc

After pkzip finishes: Turn computer – Off

Remove 8 mm tape, set no erase tape, label, and place in case

M200 Monitor – Off

TDL – Off

TDL Pump – Off

Applanix – Off

CCN Counter - Off

Remove PC Card from Applanix

Research Power – Off

TAMDAR DC power breaker – Out

Remove CCN pads from counter, clean chamber, replace cover