GCPEx 2012 Flight Engineer Checklist - Updated January 9, 2012

# Before Flight

## Set watch to current GMT time.

## Have digital camera.

## Have USB sticks and PCMCIA card.

## Have note books with check list.

Remove CPC Butanol Bottle.

Set Nevzorov control box to the correct settings for the chosen hotwire temperatures (match the stickers).

# Before Engine Start:

## Make sure memory card is in the Applanix Unit.

## Make sure PCMCIA card is in the M300.

## Make sure all rack power controls are on assigned inverters (especially 2nd rack)

# After Engine Start:

## Push all AC breakers (5 breakers)

## M300 Power – On

Push in all DC instrument and anti-ice breakers

Applanix Power – On

## TDL and Back-Right Rack Power Bar – On

## Run timesync.awk script on M300 computer terminal window – ‘timesync.awk’

Give CPC initial settings command – type ‘setscc’ into a terminal window

Start M300 software – type ‘m300’ or ‘go’ into a terminal window

Data File Check (Check that data is being saved to hard disk).

Bring up M300 Status Window (Use F1 to select), note data <filename>.

Bring up terminal window, ‘cd /2010/m300data’, ls –l <filename>, note size.

Ensure a file being written to (F1 screen) and that its size is not zero.

## Tell Pilots: Ready to Taxi

## M300 F3 Status Checks

Check static pressure, note value.

### Check air temperature, note value.

### Check dew point temperature, note value.

### Check Goodrich OID Power Switch.

Check Goodrich OID switch settings (gain 1 up and gain 0 down).

Check Goodrich OID, note voltage values (< 0.7 volts)

### Check CDP, note reference voltage (~ 5.0 volts).

### Check CPC, note average concentration, ‘No CPC Data Interval’ (1), and flow rate (~1 Lpm).

### Check Laser Hygrometer, note dew point temp and flow rate (~ 8.5 Lpm).

### Check the 2-DC; note the End Element voltages (> 0.5 volts)

Check Serial Data Screen, note data acquisition status

Check Goodrich Ice Detector, note MSO Frequency and Operational State

Check CIP, note Diode Voltages

# After Takeoff:

## Open the shutter for the Goodrich OID.

## King Probe power switch and Heater switch– On

## Nevzorov Power and Heaters – On

Note temperature settings on Nevzorov box

Note voltage values for all 8 connectors (>0.0 volts)

## Before Landing:

## King Probe – Off

## Nevzorov – Power and Heaters Off

## Close the shutter for the Goodrich OID.  Note position.

# After Landing:

## M300 Data System

### Quit M300 Software File/Exit (Do not save when asked).

Turn M300 off

## Applanix – Off

## DC power breakers – Out

## Check all computers are off

## Pull all AC breakers

# After Flight

# Copy M300 flight data onto PCMCIA card (/dos/c directory).

## Remove M300 and Applanix PCMCIA card from airplane.

| Command | Description | Command | Description |
| --- | --- | --- | --- |
| Alt F1 | Hide Window | CTL F1 | PCASP Pump |
| F1 | Control Window | CTL F2 | Pitot Selection |
| F2 | Profiles | CTL F7 | Map Zoom In |
| F3 | Text Display | CTL F8 | Map Zoom Out |
| F4 | Strip Charts 1 | CTL F9 | Map Center |
| F5 | Strip Charts 2 | CTL F10 | Clear Map |
| F6 | Spectrum Plots | CTL F11 | Previous Desktop |
| F7 | Flight Track | CTL F12 | Next Desktop |
| F8 | Combine Spectrum | CTL ALT F1 | Shutdown |
| F9 | 2D Images | CTL ALT F5 | Quit |
| F10 | Help Screen |  |  |
| F11 | Main Screen |  |  |
| F12 | M300 Logger |  |  |

| KVM Switch # | Computer |
| --- | --- |
| 1 | CPI |
| 2 | HVPS-3 |
| 5 | M300 screen |

Manually Update M300 time:  quit M300 software and adjust time (su && date HHMM.SS && rtc –s hw && exit), restart m300 software

Set Time Code Generator Time Zone (UTC): in M300 terminal window type: ‘serread /dev/ser10 -8 –n –b 19200 && s+000’

# GCPEx CPI & HVPS-3 Flight Engineer Checklist - Updated January 9, 2012

# After Engine Start:

## CPI Computer – On

## HVPS-3 Computer – On

Wait for M300 computer to fully boot

HVPS-3

Run Time_Diff_UND.bat script (check time difference with the M300).  Note difference.

If (t > 2 sec, re-run Sync_Time_UND.bat script.  Check time difference.  Note difference.

Double click HVPS software icon on desktop (Spec2d.exe)

Turn HVPS power switch on face of computer to ON

In HVPS software, Click on red triangle ‘Record’ button, note file name.

Check getting TAS from M300 computer

## CPI System

- Run Time_Diff_UND.bat script (check time difference with the M300).  Note difference.

- If (t > 2 sec, re-run Sync_Time_UND.bat script.  Check time difference.  Note difference.

CPI Power Supply – On

Communications test

#### Open PC2MA test software (icon on desktop)

#### Go to File, then click GO

#### If test does not respond, restart computer only and run PC2MA again

#### After PC2MA responds, close PC2MA

Start CPI software

Set laser settings under Settings:

#### PDS45 laser, PDS90 laser, & Main laser:  4095   Spectral Width: 2048.

Click on Start Probe button

During Flight

Make sure optical instrument port stays clear (window)

# After Landing:

## CPI – Stop Probe, exit data acquisition software, shut down probe and computer

## HVPS-3 –

Hit “Stop” button (Red circle w/ ‘X’ in middle)

Click “File”, then “Exit”

Shut down probe and computer

# After Flight:

## Copy CPI and HVPS-3 data onto flash drive.

## Transfer data from flash drive to laptops