Goodrich 2011 Flight Engineer Checklist - Updated June 23, 2011

# Before Flight

## Set watch to current GMT time.

## Have digital camera.

## Have USB sticks and PCMCIA card.

## Have note books with check list.

Remove CPC Butanol Bottle.

Set Nevzorov control box to the correct settings for the chosen hotwire temperatures.

# Before Engine Start:

## Make sure memory card is in the Applanix Unit.

## Make sure PCMCIA card is in the M300.

## Make sure all rack power controls are on assigned inverters (especially 2nd rack)

# After Engine Start:

## Push all AC breakers (5 breakers)

## M300 Power – On

Push in DC instrument and anti-ice breakers

Applanix Power – On

## TDL and Back-Right Rack Power Bar – On

## Run timesync.awk script on M300 computer terminal window – ‘timesync.awk’

Give CPC initial settings command – type ‘setscc’ into a terminal window

Start M300 software – type ‘go’ into a terminal window

Data File Check (Check that data is being saved to hard disk).

Bring up M300 Status Window (Use F1 to select), note data <filename>.

Bring up terminal window, ‘cd /2010/m300data’, ls –l <filename>, note size.

Ensure a file being written to (F1 screen) and that its size is not zero.

## Tell Pilots: Ready to Taxi

## M300 F3 Status Checks

Check static pressure, note value.

### Check air temperature, note value.

### Check dew point temperature, note value.

### Check Goodrich OIDC Power Switch, note position.

Check Goodrich OIDC gain switch settings (three switches), note positions.

Check Goodrich Optical Ice Detector, note voltage values (< 0.7 volts)

### Check CDP, note reference voltage (~ 5.0 volts).

### Check CPC, note average concentration, ‘No CPC Data Interval’ (1), and flow rate (~1 Lpm).

### Check Laser Hygrometer, note dew point temp and flow rate (~ 8.5 Lpm).

### Check the 2-DC; note the End Element voltages (> 0.5 volts)

Check Serial Data Screen, note data acquisition status

Check Goodrich Ice Detector, note MSO Frequency and Operational State

Check CIP, note Diode Voltages

# Before Takeoff:

## Open the shutter for the Goodrich Optical Ice Detector.

Check that Overflow light on Goodrich OID goes out (If not, cycle power)

# After Takeoff:

## King Probe power switch and Heater switch– On

## Nevzorov Power and Heaters – On

Note temperature settings on Nevzorov box

Note voltage values for all 8 connectors (>0.0 volts)

## Before Landing:

## King Probe – Off

## Nevzorov – Power and Heaters Off

# After Landing:

## Close the shutter for the Goodrich Optical Ice Detector.

## M300 Data System

### Quit M300 Software File/Exit (Do not save when asked).

Turn M300 off

## Applanix – Off

## DC power breakers – Out

## Check all computers are off

## Pull all AC breakers

## Ensure the shutter for the Goodrich Optical Ice Detector is closed.  Note position.

# After Flight

## Copy M300 flight data onto PCMCIA card (/dos/c directory).

## Remove M300 and Applanix PCMCIA card from airplane.

| Command | Description | Command | Description |
| --- | --- | --- | --- |
| Alt F1 | Hide Window | CTL F1 | PCASP Pump |
| F1 | Control Window | CTL F2 | Pitot Selection |
| F2 | Profiles | CTL F7 | Map Zoom In |
| F3 | Text Display | CTL F8 | Map Zoom Out |
| F4 | Strip Charts 1 | CTL F9 | Map Center |
| F5 | Strip Charts 2 | CTL F10 | Clear Map |
| F6 | Spectrum Plots | CTL F11 | Previous Desktop |
| F7 | Flight Track | CTL F12 | Next Desktop |
| F8 | Combine Spectrum | CTL ALT F1 | Shutdown |
| F9 | 2D Images | CTL ALT F5 | Quit |
| F10 | Help Screen |  |  |
| F11 | Main Screen |  |  |
| F12 | M300 Logger |  |  |

| KVM Switch # | Computer |
| --- | --- |
| 1 | CPI |
| 2 |  |
| 3 |  |

Manually Update M300 time:  quit M300 software and adjust time (su && date HHMM.SS && rtc –s hw && exit), restart m300 software

Set Time Code Generator Time Zone (UTC): in M300 terminal window type: ‘serread /dev/ser10 -8 –n –b 19200 && s+000’

# Goodrich 2011 CPI Flight Engineer Checklist - Updated June 24, 2011

# After Engine Start:

## CPI Computer – On

Wait for M300 computer to fully boot

## CPI System

Run Sync_Time_UND.bat script

CPI Power Supply – On

Communications test

#### Open PC2MA test software (icon on desktop)

#### Go to File, then click GO

#### If test does not respond, restart computer only and run PC2MA again

#### After PC2MA responds, close PC2MA

Start CPI software

Set laser settings under Settings:

#### PDS45 laser, PDS90 laser, & Main laser:  4095   Spectral Width: 2048.

Click on Start Probe button

# After Landing:

## CPI – Stop Probe, exit data acquisition software, shut down probe and computer

# After Flight:

## Copy CPI data onto flash drive.

## Transfer data from flash drive to laptops