OLYMPEX 2015 Flight Engineer Checklist - Updated 2015/10/28

# Before Flight:

## Run Sync_time.bat on all computers

## Set phone/watch to current GMT time.

## Have digital camera.

## Have USB sticks and PCMCIA card.

## Have note books with check list.

## Set Nevzorov control box to the correct settings for the chosen hotwire temperatures (match the stickers) [110C for flight, 70C for ground]

# Before Engine Start:

## Make sure memory card is in the Applanix Unit.

## Make sure PCMCIA card is in the M300.

## Make sure all rack power controls are on assigned inverters (especially 2nd rack)

# After Engine Start:

## Push all AC breakers (6 breakers)

## M300 Power – On

## Applanix Power – On

## TDL and Back-Right Rack Power Bar – On

## Run timesync.awk script on M300 computer terminal window – ‘timesync.awk’

## Push in all DC instrument and anti-ice breakers

## Start M300 software – type ‘m300’ or ‘go’ into a terminal window

### Data File Check (Check that data is being saved to hard disk).

#### Bring up M300 Status Window (Use F1 to select).  Note data <filename>.

#### Bring up terminal window, ‘cd /2015/m300data’, ls –l <filename>.  Note size.

#### Ensure a file being written to (F1 screen) and that its size is not zero.

## Check that the “ASCII Text” button is pushed in on M300 main (F1) screen

## Tell Pilots: Ready to Taxi

## M300 F3 Status Checks

### Check static pressure.  Note value.

### Check air temperature.  Note value.

### Check dew point temperature.  Note value.

### Check CDP.  Note reference voltage (~ 5.0 volts).

### Check the 2-DC.  Note the End Element voltages (> 0.5 volts)

### Check CSI, note data acquisition status

### Check TDL Laser Hygrometer.  Note dew point temp and flow rate (~ 8.5 Lpm)

### Check the Applanix.  Note latitude and longitude

### Check Goodrich Ice Detector.  Note MSO Frequency and Operational State

### Check Gust Boom data.  Note pressures

### Check Serial Data Screen.  Note data acquisition status

# After Takeoff:

## King Probe power switch and Heater switch– On

## Nevzorov Power and Heaters – On

## Note voltage values for King probe signal and slave (slave volt ~ 5 volts)

## Note voltage values for all 8 Nevzorov connectors (>0.0 volts)

# Before Landing:

## King Probe – Off

## Nevzorov – Power and Heaters Off

# After Landing:

## M300 Data System

### Quit M300 Software File/Exit (Do not save when asked).

### Turn M300 off

## Applanix – Off

## DC power breakers – Out

## TDL and TDL pump - Off

## Check all computers are off

### 2DS, HVPS3, HVPS3 #2, & CPI

## Pull all AC breakers

# After Flight:

## Copy M300 flight data onto PCMCIA card (/dos/c directory).

## Remove M300 PCMCIA card from airplane.

| Command | Description | Command | Description |
| --- | --- | --- | --- |
| Alt F1 | Hide Window | CTL F1 | PCASP Pump |
| F1 | Control Window | CTL F2 | Pitot Selection |
| F2 | Profiles | CTL F7 | Map Zoom In |
| F3 | Text Display | CTL F8 | Map Zoom Out |
| F4 | Strip Charts 1 | CTL F9 | Map Center |
| F5 | Strip Charts 2 | CTL F10 | Clear Map |
| F6 | Spectrum Plots | CTL F11 | Previous Desktop |
| F7 | Flight Track | CTL F12 | Next Desktop |
| F8 | Combine Spectrum | CTL ALT F1 | Shutdown |
| F9 | 2D Images | CTL ALT F5 | Quit |
| F10 | Help Screen |  |  |
| F11 | Main Screen |  |  |
| F12 | M300 Logger |  |  |

| KVM Switch # | Computer |
| --- | --- |
| 2 | HVPS-3 |
| 3 | 2D-S |
| 4 | Main M300 |
| 5 | Secondary M300 |

Manually Update M300 time:  quit M300 software and adjust time (su && date HHMM.SS && rtc –s hw && exit), restart m300 software

Set Time Code Generator Time Zone (UTC): in M300 terminal window type: ‘serread /dev/ser10 -8 –n –b 19200 && s+000’

CPI, HVPS-3 and 2D-S Systems

# After Engine Start:

## Wait for KVM switch to power on (Make sure blue light is vertical on KVM switch)

## CPI Power Supply – On (Before computer)

## Wait for M300 computer to fully boot

## HVPS-3 Computer – On

## HVPS-3 Computer #2 - On

## 2D-S Computer (2nd Rack Switch) - On

## CPI Computer - On

CPI:

## Run Time_Diff_UND.bat script. Note time difference.

### If Δt > 2 sec, re-run Sync_Time_UND.bat script.  Check and note time difference.

## Communications test:

### Open PC2MA test software (shortcut icon on desktop)

### Go to 'File', then click 'GO'

### If test does not respond, restart computer only and run PC2MA again

### After PC2MA responds, close PC2MA

## Start CPI software

### If PC2MA software test failed and probe will not initialize, probe may be overheating.  Pull AC breakers on CPI power box and restart.  May not function until there is airflow through instrument (takeoff).

## Set laser settings under Settings: BIG SETTINGS Button

## Set PDS45 laser, PDS90 laser, & Main laser to 4095.  Set Spectral Width to 2048.

## Click on Start Probe button

HVPS-3-UND (1st rack):

## Time_Diff_UND.bat script (Compare with the M300).  Note difference.

### If Δt > 2 sec, re-run Sync_Time_UND.bat script.

### If Sync_Time_UND.bat is not working, set time manually.

## Double click HVPS software icon on desktop (Spec2d.exe)

## Turn HVPS power switch on face of computer to ON

## In HVPS software, Click on red triangle ‘Record’ button.  Wait for program to respond.  Note file name.

## Check getting TAS from M300 computer.  Note TAS

## Check diode voltages (1.5 < diode voltage < 4.0 V)

## Check mask settings (current mask should be set to ‘1-FFFF’ and the bar next to the mask name should be all black)  Change mask name to '1-FFFF' and hit 'Modify' to change the mask.  Click on the ‘Send Command Packet’ button.

2D-S:

## Run Time_Diff_UND.bat script (Compare time with the M300). Note difference.

### If Δt > 2 sec, re-run Sync_Time_UND.bat script.

#### If Sync_Time_UND.bat is not working, set time manually.

## Turn on 2D-S power, Click on red triangle 'Record' button.  Note file name.

## Check TAS is being sent from M300 computer.  Note TAS

## Check diode voltages (1.5 < diode voltage < 4.0 V)

## Check mask settings (current mask should be set to ‘1-FFFF’ and the bar next to the mask name should be all black)  Change mask name to '1-FFFF' and hit 'Modify' to change the mask.  Click on the ‘Send Command Packet’ button.

## Check Right Outboard switch is set to Inverter 4 (2DS heaters)

CSI:

## Click on KVM channel 4 for 2DS/CSI computers

## Click on VNC address book (password is ‘g1’)

## Click on CSI

## CSI 2.1.0

## Power to the CSI

## Wait for computer to boot up

## Click on Serial Tab and click on save data.  Note file name.

## Click on Write Data Tab and change save data to every 180 minutes for both CSI and TDL

## Click on Start New File button now for both CSI and TDL.  Note new file names.

## In the Program Tab, check the System Status to make sure Diamond, Sensorary, Hygro, and Serial Out are illuminated

## Open bottle valve until regulator has a pressure of 25 psi.

HVPS-3-#2 (Cappuccino; 2nd rack) (MUST be turned on AFTER HVPS-3-UND!):

## Time_Diff_UND.bat script (Compare with the M300).  Note difference.

### If Δt > 2 sec, re-run Sync_Time_UND.bat script.

### If Sync_Time_UND.bat is not working, set time manually.

## Double click HVPS software icon on desktop (Spec2d.exe)

## Turn HVPS power switch on face of computer to ON

## In HVPS software, Click on red triangle ‘Record’ button.  Wait for program to respond.  Note file name.

## Check getting TAS from M300 computer.  Note TAS.

### If not getting TAS from the m300, click on the ‘Tools’ menu and then click on ‘TAS Source’.  Click on the ‘TAS/Pitot’ button, save the change, and then exit the software.  Open the HVPS software again and change the TAS source back to ‘NASA DC-8’.  Note TAS and new filename.

## Check diode voltages (1.5 < diode voltage < 4.0 V)

## Check mask settings (current mask should be set to ‘1-FFFF’ and the bar next to the mask name should be all black)  Change mask name to '1-FFFF' and hit 'Modify' to change the mask.  Click on ‘Send Command Packet’ button.

# During Flight:

## Check particle display to ensure there are particles with in cloud.  The mask needs to be a black bar, set mask differently if necessary.

## Check for streaks in the particle image data.  If so, increase laser voltage to 3200 for horizontal channel and 3000 for vertical channel (element voltages should be around 4)

## Check Spec2DS and SpecHVPS3 for an increase in file size.

## Check below the images that the bytes are increasing.

## Check the top of the window (blue bar) to see “Recording”. If “Recording” is not at the top, press record (red triangle) - there will then be two files for that day. [Write down the new file name]

## If need more heat on CPI:

### Click on 'Setting' on top menu bar, then click on 'Advanced Control and Settings'

### Cick on the bubble that says 'Central Sampling Tube' or 'Aft Sampling Tube', then click the 'Apply' button right away.

### Repeat procedure to turn off these heaters.  Make sure the Central and Aft Sampling Tube heaters are turned off before landing (causes problems on start-up otherwise)

## Check CSI bottle regular pressure about every 5 minutes

# After Landing:

CPI:

## Stop probe, exit data acquisition software, shut down probe and computer

HVPS-3

## Hit “Stop” button (Red circle w/ ‘X’ in middle)

## Click “File”, then “Exit”

## Shut down probe and computer

2D-S

## Hit “Stop” button (Red circle w/ 'X' in middle)

## Click “File”, then “Exit”

## Shut down probe and computer

## Set 2nd Rack, 1st Switch (Bottom Powerstrip) to 0 (zero)

CSI:

## Click STOP in the Program Tab and turn off the CSI program

## Shut the CSI cylinder valve and let the flow in the pressure meter drop.  Note the pressure in the cylinder.

# After Flight:

## Copy HVPS-3, HPVS-3 #2, CPI, and 2D-S data onto flash drives labeled for each.